## Slide 1: Digital Audio Fundamentals

## Slide 2: What is Sound?
Sound is when air molecules are disturbed and set in motion
Three stages of sound
Creation
Transmission
Reception

## Slide 3: Parameters of sound
Amplitude
The amount of energy in the sound
Waveform
The shape of a regular vibration
Frequency
Speed of regular vibration (vibs / sec)
Spectrum
The distribution of component frequencies

## Slide 4: Waveform
Frequency = number of complete waveforms per sec
Unit of measurement = Hz
kHz is 1000 Hz

## Slide 5: Waveform
Amplitude => height of waveform
Measured as Intensity (Watts/m2)
Threshold of hearing is 10-12 W/m2 (or 0 dB)
Threshold of pain is 1 W/m2 (or 120 dB)

## Slide 6: Frequency / Pitch
Perception of Frequency is exponential
Pitch is the ratio of two frequencies
  A4 => 440 Hz
  A5 => 880 Hz
  2:1 is Octave
  3:2 is Fifth

## Slide 7: The Analog Process
Reception of Sound
  Human eardrum is moved by air vibrations
  Eardrum moves “analogously” to the sound

## Slide 8: Analog Recordings
Microphone has diaphragm with magnet attached
As diaphragm moves “analogously” to sound, moving magnets create “analog” electronic signal
Signal travels down cable to magnetic tape

## Slide 9: Digitizing Sound
When analog signal is recorded digitally:
  Signal enters an Analog-to-Digital-Converter (ADC)
  Measures instantaneous amplitude of input signal
  Outputs stream of numbers

## Slide 10: Digital Audio

## Slide 11: Digital vs Analog
Analog is continuous
Digital is discrete
  Need lots of “samples” of the analog signal
  Need good representation of amplitude values

## Slide 12: Terminology for Digital Audio
Sampling Rate
  The number of samples / sec the ADC or DAC processes
  Sampling Rates for
    CD = 44,100 Hz (44.1 kHz)
    DVD = 48,000 Hz (48 kHz)

## Slide 13: Sampling Rate Errors
Sampling has limits in the frequency domain
Nyquist Theorem
  A discrete time sequence of a continuous signal contains enough information to accurately reproduce the signal when the sampling rate () is twice the highest frequency in the original signal

## Slide 14: Sampling Rate Errors
Nyquist Rate - The minimum acceptable sampling rate (2 * frequency).
Nyquist Frequency - The highest frequency component that can be correctly sampled.

## Slide 15: SR Error: Aliasing
“Wagon-wheel” effect
  As wheel moves faster, it appears to move faster
  As wheel speed approaches Nyquist limit, wheel appears to slow down, stop and then reverse

## Slide 16: The Wagon Wheel Effect

## Slide 17: Aliasing Effect
As measured frequency rises past the playback frequency decreases at same rate

## Slide 18: Terminology for Digital Audio
Resolution or bit-size
  The size in bits of each sample
  Binary storage is in 0s and 1s (bits)
  8-bit datum => 0010 0111
    possible states / values
    only 256 (28) values between -1 and 1
  16-bit datum => 0101 1101 1111 0110
    65,538 possible values between -1 and 1

## Slide 19: Quantization Error
Low bit size => high quantization error
High bit size => low quantization error

## Slide 20: Quantization Error
Bit Depth - The number of bits used for each sample which determines the precision with which you can represent the sample amplitudes.
Distortion - The unwanted part of the audio signal that is related to the true signal.

## Slide 21: More Terms To Know
Gain – Initial volume setting of a sound source.
Boost – Raising the gain amount.
Attenuate – Lowering the gain amount.
Phase – The polarity of a signal and how it relates to the polarity of another signal.
Bounce – Rendering a digital audio signal into a new digital audio file.

## Slide 22: More Terms To Know
Plugin – Small application that runs inside of your DAW that processes audio in some way, either as an effect or some kind of utility tool.
Root Mean Square (RMS) – The average loudness of a signal
Decibel – Unit of measurement that describes the loudness of a signal