## Slide 1: Representing Musical Information
MUS 4745

## Slide 2: What is Musical Data?
Notes
  Pitch, dynamics, duration
Instrument
  Timbre, range, color, location

## Slide 3: What is Musical Data?
Time-variant information
  Phrasing, crescendo/decrescendo
  Tempo, articulations
  Information that ties multiple notes together
Language information
  Lyrics
  Stage directions
Meta information
  Composer, year of composition, instrumentation

## Slide 4: What is MIDI?
Musical Information Digital Interface
  Hardware specification for interface devices
  Standard communication protocol for musical information
  Standard storage format for data
This Photo by Unknown Author is licensed under CC BY-SA

## Slide 5: Why use MIDI?
Sending control messages from musical instrument analogs (keyboards, percussion, wind controllers) to synthesizers and computers
Recording and playback of musical performance
This Photo by Unknown Author is licensed under CC BY-NC-ND

## Slide 6: Why not MIDI?
Not a complete representation of musical information
  It only represents musical performance information
  Does not address musical meta- or global information
It is NOT a medium for digital audio

## Slide 7: Why MIDI?
A little history of digital instruments in necessary
  Analog Synthesizers (1960s-70s)
    Moog, Roland, Oberheim
    Voltage-controlled oscillators, amplifiers
  Late 1970s - Early 1980s
    Digital control of analog synthesizers
    Sequential Circuits (Prophet 5), Korg, Roland, Oberheim, Yamaha
  Interoperability was a problem
    CV values for each manufacturer were different

## Slide 8: Why MIDI?
Digital Synthesizers were on the way!
  Yamaha DX7 released in 1983
  First mass-produced digital synthesizer
    Most successful synthesizer EVER!
Everybody else tried to compete
  Casio, Oberheim, Korg, Kawai, Prophet, Akai, Ensoniq

## Slide 9: Why MIDI?
Economic Pressure
  Musicians wanted to connect synths together so you could play one of many synths with one keyboard
  Manufacturers had proprietary communication systems
    You had to buy all your synths from the same manufacturer
  Competitive pressure on instrument manufacturers drove the collaboration
  Universal Synthesizer Interface…

## Slide 10: Why MIDI?
1982
  Roland, Yamaha, Kawai, Korg, Sequential Circuits agreed to collaborate on a method to connect their devices
1983
  Published Musical Instrument Digital Interface (MIDI)
  Designed for communication between instruments of different manufacturers
  Demonstration of connected devices at the Jan 1983 NAMM show

## Slide 11: Why MIDI?
1984 - Macintosh computer
1985 - MIDI protocol
  people realized that computers could “read” MIDI data
  new kind of music software - the “sequencer”

## Slide 12: Why MIDI?
MIDI Sequencers
  Read, write, playback MIDI data in time synchronous fashion
  Tape deck metaphor
In late 1980s, computer chips became fast enough to handle real-time digital audio
  Digital audio recording and editing apps
  By late 1990s, DAR and MIDI apps merged

## Slide 13: MIDI Hardware
Hardware specifications
  Uni-directional communication
  MIDI In, MIDI Out, MIDI Thru
  DIN 5-pin connections
  31,250 kbits / second
This Photo by Unknown Author is licensed under CC BY-SA

## Slide 14: MIDI Hardware
MIDI Interfaces
MIDI Controllers
  Keyboards, Wind Controllers, Percussion controllers
  Non-traditional controllers (gloves, theremin)
MIDI Synthesizers
This Photo by Unknown Author is licensed under CC BY-SA
This Photo by Unknown Author is licensed under CC BY-NC
This Photo by Unknown Author is licensed under CC BY-SA

## Slide 15: Bits & Bytes
Bits
  Bits are binary digit spaces (0 or 1)
Byte
  a single piece of data (datum)
  Each byte is sized by the number of bits
  8-bit datum can represent 256 states (2^8)
  16-bit datum can represent 65,536 states (2^16)

## Slide 16: MIDI Protocol
8-bit data structure
Standardized set of “message” types
  Note On
  Note Off
  Continuous Controller
  Program Change
Each message type consists of one, two or three bytes

## Slide 17: MIDI Protocol
Messaging is best represented in Hexadecimal (base 16)
  Base 16
  0, 1, 2, 3, 4, 5, 6, 7, 8, 9, A, B, C, D, E, F
  Use $ or 0x as prefix
  $90 = 1001 0000 = 2^7 + 2^4 = 128 + 16 = 144

## Slide 18: MIDI Messages
MIDI messages contain a status byte (or command byte) and data byte(s)
Status bytes have two components
  MSB = MIDI Command
  LSB = MIDI “channel”
Generic message structure is:
$command-channel $data1 $data2
1001 0000 = 9 => MSB
1001 0000 = 0 => LSB
$90 => NoteOn, channel 1

## Slide 19: Note On
Note On - $9x $kk $vv
  x = channel number
  kk = MIDI key (0 - 127)
    Middle C = 60
  vv = Velocity (0 - 127)
    Velocity 0 => silent

## Slide 20: Note Off
Note Off - $8x $kk $vv
  x = channel number
  kk = MIDI note number
  vv = velocity
    assumed to be zero, usually ignored

## Slide 21: Aftertouch
Aftertouch = $Ax $kk $vv
  x = channel number
  kk = key number
  vv = velocity

## Slide 22: Continuous Control
Control change = $Bx $cc $vv
  x = channel number
  cc = controller (0 - 119)
  vv = control value
Used to change synthesis parameters during execution (i.e. vibrato, timbre shift)

## Slide 23: Program Change
Program Change = $Cx $pp
  x = channel number
  pp = program number
Recall saved synthesis patch to synthesizer

## Slide 24: Pitch Bend
Pitch bend = $Dx $aa $bb
  14-bit number up or down
  $aa = least significant byte ($00 - $EF)
  $bb = most significant byte ($00 - $EF)
  Pitch bend value = $bbaa

## Slide 25: System Exclusive
System Exclusive
End of Exclusive Message
Sends manufacturer-specific information to the synthesizer

## Slide 26: Real-time Messages
Timing Clock - $F7
  24 times per quarter note when in synch mode
Active Sensing - $FE
  sent up to 300 ms apart
Reset - $FF
  Return all values to zero

## Slide 27: MIDI & Csound
MIDI is a universal protocol and can be used with Csound
Csound can
  Read MIDI files to control its virtual synthesizers
  Use MIDI representation as score values
  Send MIDI information to other applications or off-board synthesizers (but why?)